## Slide 1: THE R’s (REDUCE, REUSE AND RECYCLE) FOR CLIMATE RESILIENCE WASTEWATER SYSTEMS IN BARBADOS (3R-CReWS)
Technical working group meeting
18 February 2022

## Slide 2
Notes: Standardised Precipitation Index (12-month period) from monthly precipitation as projected by an ensemble of CMIP6 models with the SSP2-4.5 scenario. The grey shaded area represents the current climatological normal

## Slide 3
Notes: SPI over the period 1991 – 2020 is almost the mirror image of observed salinity in wells. Periods of drought (negative SPI values, red) correlate with increasing salinity.

## Slide 4: 3R-CReWS
Component 1 involves installing centralized and decentralized cluster wastewater collection and treatment systems to achieve a tertiary water-quality for multiple non-potable water reuse applications that will increase water availability and the water sector’s resilience to climate change.
Component 2 focuses on enhancing the climate resiliency and carbon-neutrality of the BSTP wastewater treatment system through the installation of renewable photovoltaic energy, and energy conservation and improved efficiency measures

## Slide 5: 3R-CReWS
Component 3 is focused on enhancing options for scaling-up wastewater reuse as well as the capabilities of technical personnel at BWA to promote sustainability.
Component 4 is focused on enhancing the enabling environment for wastewater management by advancing stakeholders’ (government, public, tourists, teachers, students, private sector/businesses, civil society) buy-inleadership and ownership

## Slide 6
IMPACT: Enhanced health, wellbeing, and productivity of Barbadians through the use of carbon neutral and climate resilient water and energy management technologies and strategies that ensures water is protected, managed, recycled, reused, and conserved |  |  | 
OUTCOMES |  |  | 
1. Enhanced availability, management and use of tertiary level treated wastewater to improve the water sector’s resilience to climate change | 2. Climate resilient net zero carbon operations achieved at BSTP | 3. Enhanced capacity and capability to support a preventative maintenance (PM) and climate resiliency programme | 4. An enabling environment is created for wastewater technologies and reuse in the public and private sectors
OUTPUTS |  |  | 
1.1 The Bridgetown Sewage Treatment Plant (BSTP) is upgraded to treat wastewater to a tertiary water-quality standard. | 2.1 Energy efficiency and renewable energy technologies are implemented | 3.1 Improved capabilities of wastewater technical personnel to operate, maintain and monitor and implement climate change adaptation planning strategies for wastewater management | 4.1 Governance and planning roadmaps updated/developed to enable wastewater reuse in the public and private sectors
1.2 Tertiary wastewater is available to supplement non-potable use |  | 3.2 A strategic plan is developed to guide the replication of the brackish water RO treatment plant along the west coast corridor | 4.2 Mechanisms developed/expanded to encourage the adoption of wastewater treatment and reuse applications by private individuals and businesses
1.3 Decision-support tools and infrastructure implemented to mitigate potential climate change risks to the wastewater collection and treatment systems |  |  | 4.3 Gender Sensitive Public Education and Awareness Campaign Implemented.
1.4 Decentralized treatment plants or cluster treatment facilities installed |  |  | 

## Slide 7: COMPONENT 1
Activities:
Install Conventional Activated Sludge Biological treatment process
Install RO membrane filtration system
Construct 9km pipeline for irrigation and aquifer recharge
Implement sewer monitoring programme – flow measurement, rain gauging equipment
Establish on-site laboratory
Implement Computerized Real-time Management System (CMMS)
Construct 2 decentralized treatment facility in Zone A – Belle Vue and Belle Tenantry
US$42Mn
Notes: BSTP to Waterford (Botanical Gardens) with take-off at Hothersal on to Friendship Plantation then turn south along ABC H’way and then turn north along Belle Road up to Lears (Roberts Manufacturing)

## Slide 8: COMPONENT 2
Activities:
Install grid-tied PV
Install automated controls
Install sludge dewatering technologies
US$3Mn

## Slide 9: COMPONENT 3
Activities:
Develop and provide specialised training to BWA (and other Ministries, Department and Agencies, as applicable)
Update SOPs and operations manual
Develop and implement risk management framework at BWA
Investigate and develop a strategic plan for the installation of RO along the west coast
US$1.6Mn

## Slide 10: COMPONENT 4
Activities:
Undertake legislative review and provide road map
Develop Water and Sanitation Master Plan
Develop private sector engagement strategies
Undertake a review and provide recommendations on an incentive programme to encourage conservation, recycle and reuse
Expand the RAFF for the adoption of waste-water treatment technologies
Re-educate key stakeholders and implement PEA campaign
Develop a project web page and social media accounts to share progress on project
US$1.4Mn